## Slide 1: Latta slots

## Slide 2: Agenda
Motivation & Overview
System Architecture & design
Randomness & win condition
Implementation
Demo
Conclusion & future work

## Slide 3: Project goals
Achieve Real-Time Responsiveness
    System must react quickly to button presses and schedule tasks predictably
Demonstrate True Randomness
    Use Hardware RNG to ensure unpredictable outcomes
Implement Clear Game Logic
    Collect four unique LEDs to win
Highlight FreeRTOS best practices
    Segregate tasks, minimal resource sharing, and low CPU usage

## Slide 4: Top level architecture
Three Task Model
  PollButtonTask
  StateMachineTask
  AnimateTask
Event-Driven
  Communicate Exclusively via FreeRTOS queues
Low Resource Contention
  Minimal shared data, mostly block waiting on queues
Deterministic Flow
  Each event is only consumed once

## Slide 5: an idiot admires complexity, a genius admires simplicity
Terry davis

## Slide 6: Design ideas & key decisions
Modular vs. Monolithic
    Chose multi-task approach for clearer separation of concerns
Event Queue Communication
    Decouples tasks, prevents blocking
State Machine Control
    Centralized logic for transitions (Idle, Spinning, Win, Lose)
Minimal CPU Usage
    Tasks sleep/block when idle

## Slide 7: Task responsibilities
PollButtonTask
Sends EVT_BUTTON_PRESS when triggered
StateMachineTask
Processes Incoming Events
AnimateTask
Receives animation requests
Maintains Game State
Decides Next Animation
Executes LED patterns
Sends EVT_ANIM_COMPLETE to the StateMachineTask

## Slide 9
DEBUG MODE SEEDING
RELEASE MODE SEEDING
WHY IT MATTERS
Uses xTaskGetTickCount() to generate a repeatable seed
Uses the hardware RNG via HAL_RNG_GenerateRandomNumber()
Guarantees game outcomes are independent
Critical for fair gaming
randomness

## Slide 10
Achieved by collecting all 4 LEDs
Landing on a duplicate results in immediate loss
Uses bitmask to track collected LEDs
Winning condition

## Slide 12
System flow
Button Trigger
PollButtonTask sends Event_t
Spin Init
StateMachineTask calls spin()
Animation Exec
Runs animations and posts Event_t
Outcome Handling
StateMachineTask processes event

## Slide 13
ACHIEVMENTS
TAKEAWAYS
EDUCATION
Developed moduler, event driven slot machine with FreeRTOS
Task Segregation
Effective Use of Hardware RNG
Clear demonstration of real-time scheduling and state management
Insights into embedded systems
conclusion

## Slide 14
Future work
ENHANCED USER INTERFACE
DATA PERSISTENCE
ADVANCED SCHEDULING
Sounds
More Dynamic LED Animations
Implement Non-Volatile Storage
Explore Dynamic Task Scheduling
Extend Design To Support More Game Features
Latta slots
14

## Slide 15
Thank you